## Slide 1: Jasper: Network Support For Scalable Financial Exchanges on the Public Cloud
Haseeb Ashfaq, Jinkun Geng, Ulysses Butler, Xiyu Hao, Daniel Duclos-Cavalcanti, Anirudh Sivaraman, Srinivas Narayana
Paper: https://arxiv.org/pdf/2402.09527
Me: https://haseeblums.github.io

## Slide 2: Benefits of Public Cloud for Financial Exchanges
Reducing constraints of physical space around the matching engine
Unprecedented scale – 1000s of participants can be supported
Low barriers to entry for launching new global markets
Various analytics/ML services residing nearby
And typical benefits of cloud: flexible resource allocation, reduced cost, offloading management etc.
Notes: We will start by addressing what are the benefits of public cloud for the financial exchanges, why should such exchanges be built on the cloud or migrated to the cloud. Traditionally, exchanges are built in colocation facilities where all the traders/market participants are connected to the exchange with an equal length wires and they are all housed in one building. In such settings, scaling the exchange beyond some point requires gaining new real estate or getting a bigger room to house the exchange server all the traders. If exchanges can be built on the cloud, we will not have such problems.

## Slide 3: Various Ongoing Efforts
Cloud providers building bespoke services
  AWS + Nasdaq partnership
  Google + CME partnership
  Research from the perspective of cloud providers: Octopus
Enabling exchanges on the existing public cloud
Connecting on-premises exchanges to the public cloud with low latency links
Cloud Provider
Cloud Tenant
Notes: Mention Singapore stock exchange building POC exchange infra on AWS

## Slide 4: Primer On Financial Exchanges
An exchange server and several market participant (MP) servers
The exchange multicasts information about market state (market data) to all MPs
The exchange also runs a matching engine (ME) which processes trade orders received from MPs
MPs use the market data to generate the orders – often competing with each other on speed
  Speculative Triggering
Orders can be bid orders, which aim to purchase an asset at a specific price, and ask orders, which aim to sell an asset at a specific price
The ME maintains a Limit Order Book (LOB) which is a record of outstanding bids and asks

## Slide 5: Primer On Financial Exchanges
Many matching algorithms exist – price time priority is widespread
Orders belonging to a price level in the LOB are sorted based on when they were received – earlier orders get priority while matching by the ME
Orders with prices closer to the mid-price have higher chances of getting matched with other orders
An LOB snapshot:

## Slide 6: Challenging Migration
Stringent networking requirements
  Heavily engineered on-premises infrastructure
  Low jitter, high fanout switches
  Equal length wires
Public cloud does not provide much network control to a tenant
  Doesn’t allow me to equalize their wires
  Cloud is best-effort characterized by non-determinism

## Slide 7: Problem
How do we architect an exchange to support efficient communication between the exchange and ~1000 participants in the public cloud?
Market data multicast
Bursty order submission
Low latency with low spatial and temporal variance for ~1K MPs
Low order latency and high order matching rate
Performance vs security trade-offs while achieving the same abstraction as of on-premises
Jasper
Exchange to MP
Strong security boundaries
MP to Exchange
Between multiple MPs &
Between exchange and MPs

## Slide 8: How does Jasper perform?
Median Multicast* latency for 1K receivers: ≤250 microseconds with a ≤1 microsecond latency difference between any two receivers
>50 % lower median latency than a previous system, CloudEx
Order submission service achieves 80+% higher order matching rate and 98% lower order latency than a naive design
Prototyped and evaluated on two clouds: AWS and GCP
* Max latency to any receiver
Notes: Results all for GCP, except AWS TGW >50 % lower latency than the latency provided by AWS TGW

## Slide 9: Jasper Overview
Market data multicast
Bursty order submission
Trust Model
An overlay tree for scaling multicast
Overlay techniques for countering various types of performance variance
Reuse the tree for scalable fan-in communication
Pacing at the tree nodes to avoid packet drops
A special priority queue for enhancing order matching rate
Various models are presented and their performance-security trade-off is discussed
Multicast | Bursty Orders | Trust
Notes: Tracker on top of slides showing which part

## Slide 10: Scalable Market Data Multicast
An overlay proxy tree helps scale to a large number of receivers while bounding the latency
Exchange
(D=2, F=10)
Multicast | Bursty Orders | Trust
Kernel bypass + ZC packet replication
Notes: With 500 bytes packets, iperf3 shows no more than 2 Gbps achievable bandwidth on AWS. So theoretically the difference between the first and the last receiver is going to be at least 180 microseconds in the DU approach.
Redo DU with DPDK Calibrate against egress

## Slide 11: Tuning Depth and Fanout
Use a simple heuristic: assume F = 10 and calculate D accordingly
Provides near-optimal results
Due to inherent non-determinism of the cloud, small changes in the configuration may not be significant
D | F | OML (μs)
2 | 32 | 282
3 | 10 | 217 (✌️)
4 | 6 | 226
N = 1000
D | F | OML (μs)
1 | 100 | 351
2 | 10 | 139 (✌️)
3 | 5 | 141
N = 100
Multicast | Bursty Orders | Trust
Notes: Could not reliably tell the two schemes apart by looking at the results. Enough noise that a simple heuristic works well enough and lands us somewhere close to the optimal result.

## Slide 12: Countering Various Performance Variations
Latency Spikes On Links
Proxy VM’s performance variation
Receiver VMs’ performance variation
Round Robin Packet Spraying
Proxy Hedging i.e., multiple parents
Two VMs per trader
Let’s discuss these two
Multicast | Bursty Orders | Trust

## Slide 13: Round Robin Packet Spraying
Exchange
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
Message ID: 0
Multicast | Bursty Orders | Trust
Notes: Show a packet going through
Animate as much as possible
dRMT talk has good animations https://anirudhsk.github.io/ppts/drmt_sigcomm.pptx MSR research talk, dissertation talk for animations

## Slide 14: Round Robin Packet Spraying
Exchange
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
Message ID: 0, 1
Multicast | Bursty Orders | Trust
Notes: Show a packet going through
Animate as much as possible
dRMT talk has good animations https://anirudhsk.github.io/ppts/drmt_sigcomm.pptx MSR research talk, dissertation talk for animations

## Slide 15: Round Robin Packet Spraying
Exchange
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
Message ID: 0, 1, 2
Multicast | Bursty Orders | Trust
Notes: Show a packet going through
Animate as much as possible
dRMT talk has good animations https://anirudhsk.github.io/ppts/drmt_sigcomm.pptx MSR research talk, dissertation talk for animations

## Slide 16: Round Robin Packet Spraying
Exchange
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
Message ID: 0, 1, 2, 3
Multicast | Bursty Orders | Trust
Notes: Show a packet going through
Animate as much as possible
dRMT talk has good animations https://anirudhsk.github.io/ppts/drmt_sigcomm.pptx MSR research talk, dissertation talk for animations

## Slide 17: Round Robin Packet Spraying
Exchange
Message ID: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, …
Multicast | Bursty Orders | Trust
Notes: Show a packet going through
Animate as much as possible
dRMT talk has good animations https://anirudhsk.github.io/ppts/drmt_sigcomm.pptx MSR research talk, dissertation talk for animations

## Slide 18: Round Robin Packet Spraying
Uncovers new/unused (virtual) paths
Each receiver has multiple paths to the root
A latency spike on a path would only impact a subset of messages
A bursts of market data has a lower chance of filling up network queues
Multicast | Bursty Orders | Trust

## Slide 19: Proxy Hedging
Exchange
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✉️
✅
Multicast | Bursty Orders | Trust
Late arriving copies
Notes: Show a packet going through
Animate as much as possible
dRMT talk has good animations https://anirudhsk.github.io/ppts/drmt_sigcomm.pptx MSR research talk, dissertation talk for animations

## Slide 20: Proxy Hedging
Each VM has multiple parent proxies
A VM receives duplicated packets from all the parents
A single parent experiencing performance variance has lower chances of affecting the latency experienced by a child VM
Significantly narrows down the latency distribution
Multicast | Bursty Orders | Trust

## Slide 21: Market Data Multicast
The performance variation countering techniques and the overlay tree enables scalable market data multicast
We further employ a hold-and-release[1] mechanism
  All the VMs have there clocks synchronized with O(10) nanoseconds accuracy
  Sender attaches deadlines to the messages and the receivers process a message at or after the deadline.
  Deadlines are an estimate of worst OWD to any receiver, calculated online.
Hold-and-release combined with Jasper performs better
Jasper enables smaller deadlines as the latency variance has been minimized
Multicast | Bursty Orders | Trust
[1] CloudEx: A Fair-Access Financial Exchange in the Cloud

## Slide 22: Remarks On (Outbound) Packet Losses
With 10K MPS, 0.008% packet lost
With 100K MPS, 1.78% packets lost
In on-premises exchanges, market data multicast uses unreliable delivery and the overall infrastructure is engineered to provide negligible packet losses
Jasper also utilizes UDP, however are the packet losses small in the cloud?
With 350K messages per second and 100 receivers, 0.007% packets lost in a 20s benchmark
With 100k MPS, not a single packet was lost
GCP
AWS
Multicast | Bursty Orders | Trust
Notes: With 350K, 460B packets, 80% egress on GCP 100k, 460B, 23% egress on GCP 100K, 460B, 37% egress on AWS 10K, 460B, 3.7% egress on AWS

## Slide 23: Inbound Communication
Order submission by market participants to the exchange
Large number of receivers simultaneously submitting orders can lead to incast-style packet drops
Utilizing the proxy tree in the reverse direction enables each node to only receive orders from a small number of children
The reduced fan-in at the exchange avoids excessive packet drops
Multicast | Bursty Orders | Trust

## Slide 24: Inbound Communication
The bursts of orders can still lead to packet drops
We need a mechanism that handles packet drops while maintaining low order latency
Pacing at proxies
Proxies sense OWD to their parents
Pace the packets if OWD increases beyond a threshold
Packet drops resolved
Packet queues form at proxies
Increases latency
Limit Order Queue
Distributed scheduling policy at all the proxies
Reorders the queues at the proxies to decrease order latency and increase order matching rate
Let’s discuss this
Multicast | Bursty Orders | Trust

## Slide 25: Limit Order Queue
Order submitted by MPs can form queues at proxies
LOQ leverages these queues to enhance performance of ME
LOQ assigns priorities to the queued orders based on how likely an order is to get matched with some other order upon its arrival at ME
The orders that have higher chances of staying in the LOB, idling the ME, will be assigned lower priority as they can afford to wait in the queues
Orders with prices closer to the mid-price of the LOB have higher chances of getting matched
Multicast | Bursty Orders | Trust

## Slide 26: Limit Order Queue
If mid-price, which is continuously changing at the exchange, is known at the proxies, LOQ can be realized
Requires broadcasting the mid-price from the exchange to all the proxies
  Extra work for the exchange, especially when it should be avoided the most – during bursts of orders
Or each proxy can maintain an approximate LOB based on the orders it relays to the ME
  Risk of a local LOB deviating from the true LOB
Multicast | Bursty Orders | Trust
Notes: During bursts, more orders, more market data to multicast already

## Slide 27: Limit Order Queue
We present a mid-price agnostic LOQ
Each proxy maintains two priority queues – a bid queue and an ask queue
The bid queue sorts the orders in the descending order w.r.t the price
The ask queue sorts the orders in the ascending order w.r.t the price
Lets visualize the LOQ
Multicast | Bursty Orders | Trust

## Slide 28: Limit Order Queue
Multicast | Bursty Orders | Trust

## Slide 29: Limit Order Queue
Multicast | Bursty Orders | Trust
Bids Queue
Asks Queue
$5
$3
$7
$9
$8
$9
Order generation timestamp
Smaller timestamp  Higher Priority
$9
ME

## Slide 30: Limit Order Queue
A bid (ask) when dequeued from LOQ for relaying to ME has the highest probability of getting matched among all the bids (asks) present in a proxy’s queue
Matchable (or soon to be so) orders jump the queues and arrive at ME
  Allows lower latency for the matched orders
  Avoids idling the ME when useful work remains to be done → Increases the ME order matching rate
Multicast | Bursty Orders | Trust

## Slide 31: Deconstructing LOQ
LOQ reorders the queues!
Does the LOQ sacrifice correctness?
Correctness
Inbound Fairness/Unfairness
Inbound unfairness formalized by a previous work:
The percentage of sequenced packets received out of order by the ME
70% Unfairness
With LOQ
Sequenced by order generation timestamp (tg)
Multicast | Bursty Orders | Trust

## Slide 32: Inbound Unfairness
The percentage of sequenced packets received out of order by the ME
Unnecessarily strict definition!
A benign scenario considered unfair acc. to this definition:
An order o1 with price closer to mid-price compared to an order o2 arrives earlier at ME while o2 was generated before o1
This is the exact scenario which the LOQ leads to!
Multicast | Bursty Orders | Trust

## Slide 33: Order-Matching Fairness
An order O will be considered unfairly treated if:
O arrives at ME and another order with the same price but a later tg has already been executed by the ME
The above definition allows the packet scheduling policies (e.g., LOQ) to send orders with different prices out of sequence!
<5% unfairness ratio with LOQ
Multicast | Bursty Orders | Trust

## Slide 34: Trust Models
An MP should be able to protect its proprietary trading algorithm from others
An exchange should not need to rely on MPs for its correct operations
  Like trusting the MPs to add order generation timestamp, or holding the multicast messages until some deadline
We consider three trust models with varying performance and security trade-offs
Performance concern: added latency and jitter due to the security boundary
Multicast | Bursty Orders | Trust

## Slide 35: Trust Models
{x, y} represents x μs of latency and y μs of jitter
Multicast | Bursty Orders | Trust
Notes: potentially binding due to Section 6801 of 15 U.S. Code in some territories

## Slide 36: Trust Models
Low jitter optimizations for Nitro Enclave:
Isolating CPUs
Pinning threads
Reducing unnecessary timer ticks (nohz_full)
Multicast | Bursty Orders | Trust

## Slide 37: Evaluation
Notes: Write out a detailed script for every slide (better way to iterate over)
Use script to rehearse, not useful to use it during the talk Typical rehearse 10 times for the first time

## Slide 38
Evaluation
Jasper outperforms AWS TGW
and direct unicasts (DU) approach

## Slide 39
Evaluation: Proxy Hedging
OML reduces
Low temporal variability
Low spatial variability

## Slide 40
Evaluation: RRPS
Reduction in OML due to RRPS
Overall, we observe lower latency variance in GCP, hence lower benefit due to our hedging schemes
Improvement due to RRPS (%) | 15.12 | 69.35 | 9.83 | 9.18
Setup
On AWS
On GCP
50p
50p
90p
90p

## Slide 41
Evaluation: Simultaneous Delivery
Jasper and CloudEx achieve (outbound) fairness
Jasper does so without increasing OML
Because it requires low holding duration
Employ hold-and-release

## Slide 42
Evaluation: LOQ
LOQ handles the bursts effectively
  Enhances order matching rate
  Decreases latency
LOQ

## Slide 43
Evaluation: LOQ
LOQ performance increases as book depth increases

## Slide 44: Next Steps
Equivalence between price time priority matching algorithm and LOQ
  LOQ is a distributed price time priority algorithm
Designing exchange from the perspective of a cloud provider
  Lower level control over the network (SmartNICs, fine grained information about data path, better guarantees)

## Slide 45
Thank you for your attention!
Questions!